## Slide 1: Containment Domains A Scalable, Efficient, and Flexible Resilience Scheme for Exascale Systems
Jinsuk Chung, Ikhwan Lee, Michael Sullivan,
Jee Ho Ryoo, Dong Wan Kim, Doe Hyun Yoon+,
Larry Kaplan*, and Mattan Erez
UT Austin, + now at HP Labs, * Cray

## Slide 2: Containment Domains A Scalable, Efficient, and Flexible Resilience Scheme for Exascale Systems

## Slide 3: Motivation and goals
Resilience bounds performance
  Resilience is a major obstacle to exascale
Containment domains: scalable efficient resilience
Hierarchical
  Preserve data where most efficient and effective
Proportional
  Tunable redundancy and recovery
  Different errors/faults handled differently
Abstract
  Portable
  Amenable to auto-tuning and analysis
CDs elevate resilience to a first-order application concern

## Slide 4: Containment domains
Single consistent abstraction
  Encapsulates resilience techniques
  Spans levels: programming, system, and analysis
Components
  Preserve data on domain start
  Compute (domain body)
  Detect faults before domain commits
  Recover from detected errors
Semantics
  Erroneous data never communicated
  Each CD provides recovery mechanism
Hierarchy
  Escalation
  Match CD and machine hierarchies
Root CD
Child CD

## Slide 5: Mapping example: SpMV
void task<inner> SpMV( in M, in Vi, out Ri){
forall(…) reduce(…) SpMV(M[…],Vi[…],Ri[…]);
}
void task<leaf> SpMV(…){
for r=0..N
for c=rowS[r]..rowS[r+1] { resi[r]+=data[c]*Vi[cIdx[c]];
prevC=c;
}
}
Matrix M
Vector V

## Slide 6: Mapping example: SpMV
Matrix M
Vector V
void task<inner> SpMV( in M, in Vi, out Ri){
forall(…) reduce(…) SpMV(M[…],Vi[…],Ri[…]);
}
void task<leaf> SpMV(…){
for r=0..N
for c=rowS[r]..rowS[r+1] { resi[r]+=data[c]*Vi[cIdx[c]];
prevC=c;
}
}

## Slide 7: Mapping example: SpMV
Matrix M
Vector V
Distributed to 4 nodes
void task<inner> SpMV( in M, in Vi, out Ri){
forall(…) reduce(…) SpMV(M[…],Vi[…],Ri[…]);
}
void task<leaf> SpMV(…){
for r=0..N
for c=rowS[r]..rowS[r+1] { resi[r]+=data[c]*Vi[cIdx[c]];
prevC=c;
}
}

## Slide 8: Mapping example: SpMV
Matrix M
Vector V
void task<inner> SpMV( in M, in Vi, out Ri){
forall(…) reduce(…) SpMV(M[…],Vi[…],Ri[…]);
}
void task<leaf> SpMV(…){
for r=0..N
for c=rowS[r]..rowS[r+1] { resi[r]+=data[c]*Vi[cIdx[c]];
prevC=c;
}
}
Distributed to 4 nodes

## Slide 9: Mapping example: SpMV
Preserve
Detect
Recover
Preserve
Detect
Recover
Preserve
Detect
Recover
Preserve
Detect
Recover
Preserve
Detect
Recover
M
V
Parent CD
Child CD
Preserve (Parent)
Detect (Parent)
Recover (Parent)
Child
Detect
Recover
Child
Detect
Recover
Child
Detect
Recover
Child
Detect
Recover

## Slide 10: Initial CD preservation API and prototype
void task<inner> SpMV(in M, in Vi, out Ri) {
cd = create_CD(parentCD);
preserve_via_copy(cd, matrix, …);
forall(…) reduce(…) SpMV(M[…],Vi[…],Ri[…]);
commit_CD(cd);
}
void task<leaf> SpMV(…) {
cd = create_CD(parentCD);
preserve_via_copy(cd, matrix, …);
preserve_via_parent(cd, veci, …);
for r=0..N
for c=rowS[r]..rowS[r+1] { resi[r]+=data[c]*Vi[cIdx[c]];
check {fault<fail>(c > prevC);}
prevC=c;
}
commit_CD(cd);
}
Preservation components prototype on Cray XK7
http://lph.ece.utexas.edu/public/CDs
API
create_CD
preserve_via_copy
preserve_via_parent
check
commit_CD

## Slide 11: Containment domains long-term design
Hardware Abstraction Layer
Runtime Library Interface
Machine
efficiency-oriented programming model
int main(int argc, char **argv)
{
main_task here = phalanx::initialize(argc, argv);
… Create test arrays here …
// Launch kernel on default CPU (“host”)
openmp_event e1 = async(here, here.processor(), n)
(host_saxpy, 2.0f, host_x, host_y);
// Launch kernel on default GPU (“device”)
cuda_event e2 = async(here, here.cuda_gpu(0), n)
(device_saxpy, 2.0f, device_x, device_y);
wait(here, e1&e2);
return 0; }
CD Annotations
resilience model
Error Reporting Architecture
ECC, status
CD control and persistence
Language integration
Compiler support
Runtime components
Hardware aspects
CD API
resilience interface
Research prototype by Cray for XK7 (Titan)

## Slide 12: Outline
Motivation and Goals
Semantics of Containment Domains
What do CDs do? When and why are they good?
  Differentiated error handling
  Analyzability
Evaluation

## Slide 13
Differentiated Error Handling

## Slide 14: State preservation and restoration
Abstract
  Optimized preservation and restoration
  Analyzed, auto-tuned
  Allows explicit application control
Hierarchical
  Match storage hierarchy
  Maximize locality and minimize overhead
Partial
  Preserve only when worth it
  Exploit natural redundancy
  Exploit hierarchy
  Enable regeneration

## Slide 15: SpMV partial preservation tuning
Natural redundancy
void task<leaf> SpMV(…) {
cd = create_CD(parentCD);
preserve_via_copy(cd, matrix, …);
preserve_via_parent(cd, veci, …);
for r=0..N
for c=rowS[r]..rowS[r+1] { resi[r]+=data[c]*Vi[cIdx[c]];
check {fault<fail>(c > prevC);}
prevC=c;
}
commit_CD(cd);
}
Matrix M
Vector V
Hierarchy

## Slide 16: Concise abstraction for complex behavior
void task<leaf> SpMV(…) {
cd = create_CD(parentCD);
preserve_via_copy(cd, matrix, …);
preserve_via_parent(cd, veci, …);
for r=0..N
for c=rowS[r]..rowS[r+1] { resi[r]+=data[c]*Vi[cIdx[c]];
check {fault<fail>(c > prevC);}
prevC=c;
}
commit_CD(cd);}
Local copy or regen
Sibling
Parent (unchanged)

## Slide 17: Detection
Abstract
  Utilize most efficient detection mechanism
  Low overhead detection: e.g., algorithm specific detection
Customized
  Replicate in time, replicate in space, algorithm specific
Heterogeneous
  Per-CD routines
  E.g., selective multi-granularity DMR

## Slide 18: Recovery
Abstract
  Utilize most efficient recovery mechanism
  Maximize local recovery
  Low overhead recovery e.g., re-materialization or regeneration
Customized
  Re-execute, ignore, re-materialize, DMR, TMR
Heterogeneous
  Per-CD routines
  E.g., selective multi- granularity DMR
  App/system specific
Compute
Preserve
Detect
Re-execution overhead
Time

## Slide 19
Analyzability

## Slide 20: Analytical Model
Leverage hierarchy and CD semantics
  Uncoordinated “local” actions
  Solve in  out
Application abstracted to CDs
  CD tree
  Volumes of preservation, computation, and communication
  Preservation and recovery options per CD
Machine model
  Storage hierarchy
  Communication hierarchy
  Bandwidths and capacities
  Error processes and rates
Execution time

## Slide 21: Power model
CDs that are not re-executing may remain idle
Actively executing a CD has a relative power of 1
A node that is idling consumes a relative power of
  In our experiments
Idle
Re-execution time
Parallel domains
Execution
Re-execution
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle

## Slide 22: Evaluation
What we evaluated
  Performance efficiency
  Energy overhead
Baseline resiliency approaches
  g-CPR: global checkpoint restart
  h-CPR: hierarchical checkpoint restart (e.g., SCR)
  Optimum interval used for each
CD advantages
  Preserve only what is needed
  Hierarchical uncoordinated
Assumptions
  Detection overhead is assumed to be zero
  Capacity of storage for preservation is infinite
  Infinite spares (quick repair)

## Slide 23: Machine and error models
Component | “Performance” | Error | Error Scaling
Core | 10GFLOP/core | Soft error | ∝ #cores
Memory | 1GB/core | ECC fail | ∝ #DRAM chips
Socket | 200GB/s /socket | Hard/OS crash | ∝ #sockets
System | Hierarchical network | Power module or network | ∝ #modules and #cabinets

## Slide 24: Workloads
Monte Carlo NT
  Embarrassingly parallel
  Infrequent communication
  Small fraction of read/write data
Iterative hierarchical SpMV
  Recursive decomposition
  Natural redundancy
  Frequent global communication
Mantevo HPCCG
  Requires little storage
  Conjugate-gradient based linear system solver
  Frequent global communication

## Slide 25: Evaluation tools
Simulator
  Executes at granularity of containment domains
  Reexecutes when error is detected
  Used to validate the analytical model
Analytical Model
  Simulation is too slow for evaluating exascale systems
  Inputs to the model: extracted from each application
    Volume of preservation, restoration, computation and communication
    Error rates
    Shape of CD structure
Validation
  Simulator and analytical model
  Prototype of preservation/restoration on Cray XK7

## Slide 26: Autotuned CDs perform well
Peak System Performance
NT
SpMV
HPCCG
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.99175 | 0.98422 | 0.98302 | 0.97237 | 0.96043 | 0.94702 | 0.9429
h-CPR, 80% | 0.98845 | 0.98064 | 0.96938 | 0.94865 | 0.90855 | 0.85606 | 0.81179
g-CPR, 80% | 0.90834 | 0.80169 | 0.58706 | 0.17499 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.99042 | 0.98738 | 0.98262 | 0.97316 | 0.95456 | 0.93866 | 0.92273
h-CPR, 50% | 0.99086 | 0.98467 | 0.97572 | 0.9592 | 0.92711 | 0.88463 | 0.84863
g-CPR, 50% | 0.92719 | 0.84165 | 0.66711 | 0.32226 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 0.99996 | 0.99984 | 0.99971 | 0.99903 | 0.99638 | 0.99338 | 0.98936
h-CPR, 10% | 0.9959 | 0.99312 | 0.98908 | 0.98158 | 0.9669 | 0.94711 | 0.92649
g-CPR, 10% | 0.96711 | 0.92764 | 0.84441 | 0.67062 | 0.32739 | 0.075116 | 0

## Slide 27: Autotuned CDs perform well
Peak System Performance
NT
SpMV
HPCCG
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.99175 | 0.98422 | 0.98302 | 0.97237 | 0.96043 | 0.94702 | 0.9429
h-CPR, 80% | 0.98845 | 0.98064 | 0.96938 | 0.94865 | 0.90855 | 0.85606 | 0.81179
g-CPR, 80% | 0.90834 | 0.80169 | 0.58706 | 0.17499 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.99042 | 0.98738 | 0.98262 | 0.97316 | 0.95456 | 0.93866 | 0.92273
h-CPR, 50% | 0.99086 | 0.98467 | 0.97572 | 0.9592 | 0.92711 | 0.88463 | 0.84863
g-CPR, 50% | 0.92719 | 0.84165 | 0.66711 | 0.32226 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 0.99996 | 0.99984 | 0.99971 | 0.99903 | 0.99638 | 0.99338 | 0.98936
h-CPR, 10% | 0.9959 | 0.99312 | 0.98908 | 0.98158 | 0.9669 | 0.94711 | 0.92649
g-CPR, 10% | 0.96711 | 0.92764 | 0.84441 | 0.67062 | 0.32739 | 0.075116 | 0

## Slide 28: SPMV, HPCCG: local recovery and partial preservation
Disk
Remote NVM
Local NVM
DRAM
Partial preservation via sibling or parent where appropriate

## Slide 29: NT: hierarchical local recovery and partial preservation
Disk
Remote NVM
Local NVM
DRAM
Partial preservation via sibling, parent, or regeneration where appropriate

## Slide 30: Autotuned CDs perform well
Peak System Performance
NT
SpMV
HPCCG
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.99175 | 0.98422 | 0.98302 | 0.97237 | 0.96043 | 0.94702 | 0.9429
h-CPR, 80% | 0.98845 | 0.98064 | 0.96938 | 0.94865 | 0.90855 | 0.85606 | 0.81179
g-CPR, 80% | 0.90834 | 0.80169 | 0.58706 | 0.17499 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.99042 | 0.98738 | 0.98262 | 0.97316 | 0.95456 | 0.93866 | 0.92273
h-CPR, 50% | 0.99086 | 0.98467 | 0.97572 | 0.9592 | 0.92711 | 0.88463 | 0.84863
g-CPR, 50% | 0.92719 | 0.84165 | 0.66711 | 0.32226 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 0.99996 | 0.99984 | 0.99971 | 0.99903 | 0.99638 | 0.99338 | 0.98936
h-CPR, 10% | 0.9959 | 0.99312 | 0.98908 | 0.98158 | 0.9669 | 0.94711 | 0.92649
g-CPR, 10% | 0.96711 | 0.92764 | 0.84441 | 0.67062 | 0.32739 | 0.075116 | 0

## Slide 31: CDs improve energy efficiency at scale
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.0063317 | 0.0087139 | 0.011899 | 0.01684 | 0.031066 | 0.034466 | 0.03948
h-CPR, 80% | 0.011686 | 0.019745 | 0.031588 | 0.054126 | 0.10065 | 0.16815 | 0.23184
gCPR, 80% | 0.10092 | 0.24736 | 0.70342 | 4.7145 | 0 | 0 | 0
Peak System Performance
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.009667 | 0.012778 | 0.017659 | 0.027499 | 0.047447 | 0.065194 | 0.083517
h-CPR, 50% | 0.0092258 | 0.015573 | 0.024881 | 0.042531 | 0.078624 | 0.13041 | 0.17836
g-CPR, 50% | 0.078529 | 0.18815 | 0.49901 | 2.1031 | 0 | 0 | 0
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 3.2383e-05 | 0.00011761 | 0.00012313 | 0.00031516 | 0.0010207 | 0.0029016 | 0.0063734
h-CPR, 10% | 0.0041141 | 0.0069317 | 0.011044 | 0.018769 | 0.034233 | 0.055844 | 0.079342
g-CPR, 10% | 0.034009 | 0.078008 | 0.18426 | 0.49115 | 2.0545 | 12.3128 | 0
NT
SpMV
HPCCG

## Slide 32: CDs improve energy efficiency at scale
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.009667 | 0.012778 | 0.017659 | 0.027499 | 0.047447 | 0.065194 | 0.083517
h-CPR, 50% | 0.0092258 | 0.015573 | 0.024881 | 0.042531 | 0.078624 | 0.13041 | 0.17836
g-CPR, 50% | 0.078529 | 0.18815 | 0.49901 | 2.1031 | 0 | 0 | 0
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.0063317 | 0.0087139 | 0.011899 | 0.01684 | 0.031066 | 0.034466 | 0.03948
h-CPR, 80% | 0.011686 | 0.019745 | 0.031588 | 0.054126 | 0.10065 | 0.16815 | 0.23184
gCPR, 80% | 0.10092 | 0.24736 | 0.70342 | 4.7145 | 0 | 0 | 0
Peak System Performance
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 3.2383e-05 | 0.00011761 | 0.00012313 | 0.00031516 | 0.0010207 | 0.0029016 | 0.0063734
h-CPR, 10% | 0.0041141 | 0.0069317 | 0.011044 | 0.018769 | 0.034233 | 0.055844 | 0.079342
g-CPR, 10% | 0.034009 | 0.078008 | 0.18426 | 0.49115 | 2.0545 | 12.3128 | 0
NT
SpMV
HPCCG

## Slide 33: 10X failure rate emphasizes CD benefits
Peak Performance
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.97429 | 0.95249 | 0.94834 | 0.91909 | 0.88349 | 0.84948 | 0.84043
h-CPR, 80% | 0.96389 | 0.93989 | 0.90594 | 0.84509 | 0.73378 | 0.59869 | 0.50114
CDs, NT | 0.020111 | 0.027491 | 0.037868 | 0.05341 | 0.09999 | 0.11288 | 0.12931
h-CPR, 80% | 0.037468 | 0.063959 | 0.10383 | 0.18331 | 0.36281 | 0.67032 | 0.99546
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.97682 | 0.96312 | 0.94625 | 0.91695 | 0.86188 | 0.81631 | 0.77161
h-CPR, 50% | 0.97135 | 0.95221 | 0.92492 | 0.87564 | 0.78093 | 0.66871 | 0.58205
CDs, SpMV | 0.023707 | 0.038222 | 0.056592 | 0.090147 | 0.15966 | 0.22445 | 0.29511
h-CPR, 50% | 0.029496 | 0.050187 | 0.081176 | 0.14202 | 0.28052 | 0.49541 | 0.71805
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 0.99981 | 0.99928 | 0.99767 | 0.99115 | 0.97793 | 0.97428 | 0.95844
h-CPR, 10% | 0.98709 | 0.97837 | 0.96563 | 0.94241 | 0.89351 | 0.83079 | 0.75137
CDs, HPCCG | 8.6689e-05 | 0.00031038 | 0.00069738 | 0.0024087 | 0.015272 | 0.018858 | 0.028328
h-CPR, 10% | 0.013076 | 0.022107 | 0.035589 | 0.061107 | 0.11918 | 0.20367 | 0.3309
Energy Overhead

## Slide 34: More in the paper
Strict vs. relaxed containment domains
Analytical model details
Error and machine model details
Additional sensitivity studies
Related work discussion

## Slide 35: Conclusion
Containment domains
  Abstract constructs for resilience concerns & techniques
  Proportional and application/machine tuned resilience
  Hierarchical & distributed preservation, restoration, and recovery
  Analyzable and amendable to automatic optimization
  Scalable to large systems with high relative energy efficiency
  Heterogeneous to match emerging architecture
Good start and exciting work ahead
  Preservation concept prototyped on Cray XK7
  Fine-grained CDs for high error rates
  Compiler optimizations and support
  Application-specific detection/elision
  PGAS support and interactions with system
  Interaction with other models (tasking, DSLs, …)
http://lph.ece.utexas.edu/public/CDs

## Slide 36: Questions?
Thank you