## Slide 1: A brief introduction to Memory system proportionality and resilience
Mattan Erez
The University of Texas at Austin

## Slide 2
With support from
  NSF Award #0954107

## Slide 3
The constraints:
  Power/energy
  Time
  Money
  Correctness

## Slide 4
Can’t work harder –
have to work smarter

## Slide 5
Can’t work harder –
have to work smarter
Efficient & Proportional

## Slide 6
Multiple constraints and needs 
Heterogeneity
asymmetry
specialization

## Slide 7
big.LITTLE and per core DvFS
  Static and dynamic asymmetry
Accelerators
  Programmable and fixed-function

## Slide 8
Throughput cores
Latency cores
Specialized cores
   proportionality of compute

## Slide 9
Great, we solved the easy part: proportional compute

## Slide 10
Programming is hard
Memory is hard

## Slide 11
The memory challenge (outline)
  Why do memory systems look the way they do?
    Efficiency and reliability
    Abstractions for architects
  Role of heterogeneity and programs
  Some interesting mechanisms
  Where do we go from here?

## Slide 12
Storage device options abound
  SRAM
  DRAM
  FLASH
  STT-/M- RAM
  PCM, Memristor, RRAM, …

## Slide 13
Architects should think in abstractions
  Research should be general

## Slide 14
The fundamentals
Cheap
Energy efficient
High capacity
Low latency
High throughput
Reliable

## Slide 15
Memory must be cheap
  Memory is already too expensive
    15 – 50% of system cost (or more)
  But, margins razor thin (commodity)
Notes:   Processor vendors like it that way
    Customers seem to as well

## Slide 16
Memory must be energy efficient
  Memory accounts for 15 – 60+% of “compute” energy and getting worse
    More capacity
    Proportional compute

## Slide 17
Memory must be high capacity
  Memory footprints keep growing
    More interesting data
    More data
    More specialized data structures

## Slide 18
Memory must be high capacity
Many chips

## Slide 19
Memory must be high capacity
Many chips
Denser mem, Fewer chips

## Slide 20
Memory must be high capacity
Many chips
Denser mem, Fewer chips
Many dice, Fewer chips
© Micron

## Slide 21
Memory composed of
  Multiple modules
  Each module with N >=1 components
  Lots of cells per component
  Each cell >= 1 bit

## Slide 22
Memory should be low latency
  Latency == performance
  Except when sufficient concurrency

## Slide 23
Low latency conflicts with
  Cheap
  Capacity
  Sometimes with
    Throughput
    Energy
    Reliability

## Slide 24
Latency components:
  Memory cell access
  Data transfer
  Queuing

## Slide 25
Latency impacted by cell access
denser/efficient  higher latency
  Small cells  sensitive circuits  slow reads
  Writes even more complicated
+ latency
– density
– cost – energy
– latency
+ density
+ cost + energy

## Slide 26
Caching to the rescue
  Store some data somewhere fast

## Slide 27
Short distances improve latency
  It’s all about the wires

## Slide 28
Short distances improve latency
  It’s all about the wires
+ latency
+ energy
– latency
– energy

## Slide 29
Short distances improve latency
  It’s all about the wires
+ latency
+ energy
– capacity
– latency
– energy
+ capacity

## Slide 30
Hierarchy to the rescue

## Slide 31
Hierarchy to the rescue
Processor

## Slide 32
Hierarchy to the rescue
Processor

## Slide 33
Memory system
  Modules, packages, components
  Arranged in a hierarchy
Each memory component
  Has hierarchy
  Has caching/buffering

## Slide 34
Latency impacted by queuing

## Slide 35
Deep queues improve locality
  Higher throughput
  Higher efficiency
  Often hurts latency

## Slide 36
Memory must be high throughput
  More and more latency hiding

## Slide 37
Memory must be high throughput
Many chips
Fewer chips
  High capacity per pin requires efficient access

## Slide 38
Packaging/interfaces improve throughput
  3D integration
  Limited capacity
TSV
Silicon
Interposer

## Slide 39
Packaging/interfaces improve throughput
  3D integration
  Limited capacity
  More hierarchy levels
TSV
Silicon
Interposer
  Heterogeneity!

## Slide 40
Latency + throughput + efficiency  parallelism

## Slide 41
Latency + throughput + efficiency  parallelism
Access cell

## Slide 42
Latency + throughput + efficiency  parallelism
Access many cells in parallel
Many pins in parallel

## Slide 43
Latency + throughput + efficiency  parallelism
Access even more cells in parallel
Many pins in parallel over multiple cycles

## Slide 44
Latency + throughput + efficiency  parallelism
Access even more cells in parallel
Many pins in parallel over multiple cycles

## Slide 45
To recap
  Locality
  Hierarchy
  Parallelism

## Slide 46
Memory must be reliable
  Written data must be recalled “correctly”

## Slide 47
Reliability challenges
  “Natural” change in cell value
  Induced change in cell value
  Read errors
  Write errors
  Wearout and defects

## Slide 48
Natural causes of value change
Probability correct
Time
Decay
  Refresh
Notes: Natural change in state
  Decay
    DRAM leakage (refresh)
    PCM, Memristor, RRAM drift
  Flips
    DRAM/SRAM/latch particle strikes
    STT MRAM state flips
  Control
    Control-related soft errors corrupt values

## Slide 49
Natural causes of value change
Probability correct
Time
Probability correct
Time
Decay
  Refresh
Flip
  ECC + scrub
Notes: Natural change in state
  Decay
    DRAM leakage (refresh)
    PCM, Memristor, RRAM drift
  Flips
    DRAM/SRAM/latch particle strikes
    STT MRAM state flips
  Control
    Control-related soft errors corrupt values

## Slide 50
Natural causes of value change
Probability correct
Time
Probability correct
Time
Decay
  Refresh / scrub
Flip
  ECC + scrub

## Slide 51
Natural causes of value change
Probability correct
Time
Probability correct
Time
  Retention control
    Less dense
    Writes slower/higher-energy
    Can use different devices
Decay
  Refresh / scrub
Flip
  ECC + scrub
Notes: Natural change in state
  Decay
    DRAM leakage (refresh)
    PCM, Memristor, RRAM drift
  Flips
    DRAM/SRAM/latch particle strikes
    STT MRAM state flips
  Control
    Control-related soft errors corrupt values

## Slide 52
Induced change in value
  Writing or reading disturbs nearby cells
  Worse for writes
  Technology and design dependent

## Slide 53
Read errors
  Because of small margins for efficiency

## Slide 54
Write errors
  Writing implies changing a state or value
  Stochastic
Probability correct
Time

## Slide 55
Write errors
  Writing implies changing a state or value
  Stochastic
  Waiting inefficient and slow
  Write error control conflicts w/ other errors
Probability correct
Time

## Slide 56
Wearout and defects
Probability correct
Time
Probability correct
Time
Probability correct
Time
Probability correct
Time

## Slide 57
Wearout and defects
  Sparing
  Extra margins
  Retirement
  Compensation (ECC)

## Slide 58
Summary: no “good” memory
  It’s all about tradeoffs

## Slide 59
Example: DRAM
  Efficient and reliable reads and writes
  Leaky
  Density problematic
  Fairly fast reads and writes
  Parallelism determined by cost
  Fast decay (short retention)
    High variability
  Rare, but important flips
  Very rare disturbs
  Slow wearout

## Slide 60
Example: FLASH
  High-energy writes
  Very dense
  Slow reads
  Very slow writes
  Parallelism determined by technology
  Very slow decay (good retention)
  Flips only on periphery
  Write disturbs problematic
  Fast wearout

## Slide 61
Example: PCM
  High-energy writes
  Dense
  Fast reads
  Fast-ish writes
  Parallelism determined by cost
  Slow decay (OK retention)
  Flips only on periphery
  Write disturbs problematic
  Fast wearout

## Slide 62
Summary of heterogeneity:
interrelated tradeoffs
  Efficiency
  Capacity
  Latency
  Bandwidth
  Parallelism (granularity)
  Reliability

## Slide 63
The role of heterogeneous processors
heterogeneous applications

## Slide 64
Proportional compute
  Latency oriented
  Throughput oriented
  Specialized

## Slide 65
Application characteristics
  Latency sensitive
  Bandwidth sensitive
  Few tasks or many tasks

## Slide 66
Application compute styles
  Batch
  Realtime
  Response time

## Slide 67
Application data usage
  Capacity
  Locality
  Precision
  Persistence

## Slide 68
Memory must be heterogeneous but illusion of homogeneity is nice

## Slide 69
The solution: Adaptive proportional memory systems

## Slide 70
The solution: Adaptive proportional memory systems

## Slide 71
Adaptive reliability

## Slide 72
Adaptive reliability
  Adapt the mechanism
  Adapt the error rate
    precision (stochastic precision)

## Slide 73
Adaptive reliability
  By type
    Application guided
  By location (83)
    Machine-state guided

## Slide 74
Example: Virtualized ECC
  Adapt the mechanism

## Slide 75
Physical Memory
Data
ECC
Virtual Address space
Low
Virtual Page to Physical Frame mapping
Page frame – x
Page frame – y
Page frame – z
Virtual page – x
Virtual page – y
Virtual page – z
Protection Level
Medium
High

## Slide 76
Physical Memory
Data
Virtual Address space
Low
Virtual Page to Physical Frame mapping
Physical Frame to ECC Page mapping
ECC
Stronger ECC
Page frame – x
Page frame – y
Page frame – z
ECC page – y
ECC page – z
Virtual page – x
Virtual page – y
Virtual page – z
Protection Level
Medium
High

## Slide 77
Physical Memory
Data
T1EC
Virtual Address space
Low
Virtual Page to Physical Frame mapping
Physical Frame to ECC Page mapping
T2EC for Chipkill
T2EC for
Double
Chipkill
Page frame – x
Page frame – y
Page frame – z
ECC page – y
ECC page – z
Virtual page – x
Virtual page – y
Virtual page – z
Protection Level
Medium
High

## Slide 78
Two-Tiered ECC

## Slide 80
Caching work great
Chart: 
| Chipkill Detect | Chipkill Correct | 2 Chipkill Correct
Normalized Execution Time | 1 | 1.0071 | 1.0098
Normalized Execution Time

## Slide 81
Bonus: flexibility of ECC
Chart: 
| Chipkill Detect | Chipkill Correct | 2 Chipkill Correct
Normalized EDP | 0.8638 | 0.8807 | 0.88753
Normalized Energy-Delay Product

## Slide 82
Example: FREE-p
  Adapt to wearout state

## Slide 83
FREE-p insights:
  Wearout is gradual
  Adapt ECC strength to wearout degree
  Limit ECC need with adaptive repair
    Retire and remap

## Slide 84
Adapt ECC strength
  Multi-tiered ECC

## Slide 85
Different cells need different protection
Chart: Years
| 0 | 0.18579956240487061 | 0.37159912480974122 | 0.55739868721461183 | 0.74319824961948244 | 0.92899781202435316 | 1.1147973744292237 | 1.3005969368340944 | 1.4863964992389649 | 1.6721960616438356 | 1.8579956240487063 | 2.0437951864535768 | 2.2295947488584473 | 2.4153943112633183 | 2.6011938736681888 | 2.7869934360730593 | 2.9727929984779298 | 3.1585925608828007 | 3.3443921232876712 | 3.5301916856925417 | 3.7159912480974127 | 3.9017908105022832 | 4.0875903729071537 | 4.2733899353120242 | 4.4591894977168947 | 4.644989060121766 | 4.8307886225266365 | 5.016588184931507 | 5.2023877473363775 | 5.388187309741248 | 5.5739868721461185 | 5.759786434550989 | 5.9455859969558595 | 6.1313855593607309 | 6.3171851217656014 | 6.5029846841704719 | 6.6887842465753424 | 6.8745838089802129 | 7.0603833713850834 | 7.2461829337899539 | 7.4319824961948253 | 7.6177820585996958 | 7.8035816210045663 | 7.9893811834094368 | 8.1751807458143073 | 8.3609803082191778 | 8.5467798706240483 | 8.7325794330289188 | 8.9183789954337893 | 9.1041785578386598 | 9.2899781202435321 | 9.4757776826484026
quick-ECC (no failure) | 127725 | 127725 | 127405 | 126986 | 126547 | 126067 | 125518 | 124927 | 124236 | 123477 | 122636 | 121712 | 120600 | 119393 | 118105 | 116615 | 115004 | 113282 | 111387 | 109202 | 106976 | 104615 | 101962 | 99099 | 96011 | 92617 | 89044 | 85193 | 81189 | 76992 | 72630 | 68114 | 63497 | 58688 | 53899 | 49139 | 44308 | 39592 | 34820 | 30307 | 25952 | 21815 | 18030 | 14460 | 11218 | 8354 | 5868 | 3868 | 2197 | 1002 | 121
quick-ECC (1 failure) | 0 | 274 | 593 | 1012 | 1449 | 1925 | 2469 | 3047 | 3718 | 4453 | 5272 | 6153 | 7206 | 8339 | 9534 | 10910 | 12362 | 13870 | 15529 | 17436 | 19287 | 21172 | 23234 | 25369 | 27593 | 29908 | 32261 | 34742 | 37017 | 39217 | 41170 | 43070 | 44558 | 45919 | 46725 | 47026 | 47010 | 46342 | 45215 | 43371 | 40891 | 37899 | 34455 | 30540 | 26386 | 21769 | 17149 | 12463 | 8058 | 4032 | 589
quick-ECC (2 failures) | 0 | 1 | 2 | 2 | 4 | 8 | 13 | 26 | 46 | 70 | 92 | 134 | 193 | 265 | 353 | 463 | 618 | 824 | 1049 | 1293 | 1633 | 2067 | 2606 | 3249 | 3981 | 4826 | 5852 | 6943 | 8304 | 9831 | 11637 | 13454 | 15449 | 17527 | 19868 | 22326 | 24608 | 26810 | 28874 | 30716 | 32143 | 32939 | 32955 | 32250 | 30500 | 27904 | 24583 | 19940 | 14542 | 8374 | 1563
slow-ECC (3 failures) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 3 | 8 | 12 | 16 | 24 | 35 | 68 | 103 | 144 | 191 | 273 | 388 | 549 | 728 | 978 | 1292 | 1691 | 2199 | 2839 | 3682 | 4667 | 5819 | 7074 | 8643 | 10550 | 12453 | 14602 | 16874 | 19008 | 20994 | 22608 | 23847 | 24330 | 23452 | 21392 | 17646 | 11571 | 2630
slow-ECC (4 failures) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 2 | 7 | 10 | 27 | 36 | 51 | 78 | 127 | 191 | 274 | 413 | 599 | 869 | 1219 | 1711 | 2335 | 3081 | 4068 | 5267 | 6592 | 8330 | 10258 | 12204 | 13930 | 15565 | 16850 | 17226 | 15915 | 12005 | 3184

## Slide 86
Fine-grain retirement is key
Chart: Year
| 0 | 0.18579956240487061 | 0.37159912480974122 | 0.55739868721461183 | 0.74319824961948244 | 0.92899781202435316 | 1.1147973744292237 | 1.3005969368340944 | 1.4863964992389649 | 1.6721960616438356 | 1.8579956240487063 | 2.0437951864535768 | 2.2295947488584473 | 2.4153943112633183 | 2.6011938736681888 | 2.7869934360730593 | 2.9727929984779298 | 3.1585925608828007 | 3.3443921232876712 | 3.5301916856925417 | 3.7159912480974127 | 3.9017908105022832 | 4.0875903729071537 | 4.2733899353120242 | 4.4591894977168947 | 4.644989060121766 | 4.8307886225266365 | 5.016588184931507 | 5.2023877473363775 | 5.388187309741248 | 5.5739868721461185 | 5.759786434550989 | 5.9455859969558595 | 6.1313855593607309 | 6.3171851217656014 | 6.5029846841704719 | 6.6887842465753424 | 6.8745838089802129 | 7.0603833713850834 | 7.2461829337899539 | 7.4319824961948253 | 7.6177820585996958 | 7.8035816210045663 | 7.9893811834094368 | 8.1751807458143073 | 8.3609803082191778 | 8.5467798706240483 | 8.7325794330289188 | 8.9183789954337893 | 9.1041785578386598 | 9.2899781202435321 | 9.4757776826484026 | 9.6615772450532731
No Correction | 1.1 | 0.971 | 0.833 | 0.656 | 0.467 | 0.255 | 0.053 | 0
SEC64 | 1 | 1 | 1 | 1 | 1 | 1 | 0.9995 | 0.9985 | 0.9955 | 0.995 | 0.993 | 0.9895 | 0.987 | 0.978 | 0.973 | 0.9615 | 0.945 | 0.9345 | 0.913 | 0.8875 | 0.851 | 0.8125 | 0.757 | 0.686 | 0.5905 | 0.4685 | 0.306 | 0.087 | 0
ECP6 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.9995 | 0.999 | 0.9965 | 0.9915 | 0.986 | 0.9715 | 0.9465 | 0.9025 | 0.835 | 0.7115 | 0.5155 | 0.185 | 0
FREE-p | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.9995 | 0.9995 | 0.9995 | 0.9995 | 0.9995 | 0.9995 | 0.9995 | 0.999 | 0.9985 | 0.998 | 0.997 | 0.9955 | 0.9935 | 0.9895 | 0.985 | 0.9775 | 0.9675 | 0.9535 | 0.9335 | 0.906 | 0.869 | 0.819 | 0.7475 | 0.643 | 0.476 | 0.1385 | 0

## Slide 87
Adaptive FG repair
Page for remapping
D/P flag
Data page
ptr
data

## Slide 88
Impact of repair and remap is gradual
Chart: Year
| 0 | 0.18579956240487094 | 0.37159912480974339 | 0.55739868721461183 | 0.7431982496194911 | 0.92899781202435883 | 1.1147973744292241 | 1.3005969368340944 | 1.4863964992389638 | 1.6721960616438467 | 1.8579956240487063 | 2.0437951864535782 | 2.2295947488584957 | 2.4153943112633192 | 2.6011938736681888 | 2.7869934360730593 | 2.9727929984779298 | 3.1585925608828012 | 3.3443921232876708 | 3.5301916856925608 | 3.7159912480974611 | 3.9017908105022832 | 4.0875903729071466 | 4.2733899353120677 | 4.4591894977168964 | 4.6449890601217181 | 4.8307886225266374 | 5.0165881849315124 | 5.2023877473363775 | 5.3881873097412445 | 5.5739868721460715 | 5.759786434550989 | 5.9455859969558356 | 6.1313855593607265 | 6.3171851217655437 | 6.5029846841704675 | 6.6887842465752652 | 6.8745838089801845 | 7.0603833713850745 | 7.2461829337899495 | 7.4319824961948795 | 7.6177820585996745 | 7.8035816210045663 | 7.9893811834094848 | 8.1751807458143073 | 8.3609803082191778 | 8.5467798706240501 | 8.7325794330289206 | 8.9183789954336721 | 9.104178557838658 | 9.2899781202434131 | 9.4757776826484026 | 9.6615772450532731
remapped blocks per page | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0010005 | 0.0035018 | 0.0070035 | 0.013007 | 0.023012 | 0.043544 | 0.069104 | 0.10721 | 0.17051 | 0.26118 | 0.39909 | 0.6195 | 0.92234 | 1.3647 | 1.9891 | 2.8086 | 3.9775 | 5.5668 | 7.6582 | 10.3358 | 13.907 | 18.6205 | 25.1513 | 34.8051 | 64

## Slide 89
Adaptive granularity (parallelism)

## Slide 90
Applications have diverse locality
Chart: 
| GUPS | canneal | linked list | mst | em3d | SSCA2 | astar | omnetpp | bzip2 | mcf | lbm | libquantum | OCEAN | streamcluster | hmmer | STREAM
1 | 245181949 | 52511826 | 363266 | 6662975 | 205358983 | 350749383 | 1850222409 | 1327878705 | 235065722 | 214903651 | 1322438731 | 50730707 | 114080 | 163620 | 34298204 | 1116
2 | 2967804 | 28871056 | 35304130 | 9849200 | 4017205 | 81374339 | 581387755 | 1869791189 | 25608892 | 1793312507 | 1561516615 | 4697626 | 145379 | 26144768 | 3375148 | 1097
3 | 31261 | 7043787 | 658 | 90447 | 1205150 | 53945357 | 628859445 | 1405231982 | 16187013 | 1348658310 | 2927707992 | 1124376 | 64079 | 46924 | 3564613 | 495
4 | 823 | 5298869 | 617 | 166888 | 5473582 | 20809956 | 290532617 | 925829430 | 11870117 | 3245033013 | 1549041366 | 2141236339 | 10432626 | 419630 | 1629924 | 545
5 | 1054 | 2976318 | 1261 | 2128463 | 47243088 | 15093904 | 157617027 | 398996749 | 9368994 | 1017739157 | 5533962 | 7328354 | 41110 | 75274 | 1017993 | 516
6 | 1071 | 933608 | 1161 | 1299945 | 31643911 | 14084831 | 94649041 | 169791840 | 8066088 | 592389685 | 1949709938 | 10958551 | 164185 | 26144491 | 910325 | 589
7 | 525 | 768233 | 603 | 2573 | 20023495 | 14982650 | 26973434 | 206669840 | 7751397 | 3124484 | 9545 | 3166177 | 100873 | 1642310 | 36791532 | 360
8 | 33554655 | 1014600 | 8512 | 132693 | 3896709 | 79573244 | 540684364 | 610553036 | 139631370 | 1186007 | 1322747460 | 88503414 | 22612420 | 226178719 | 2059785758 | 26736488
Low spatial locality
High spatial locality
~50% is referenced
1~2
3~6
7~8

## Slide 91
Coarse- or fine-grained memory access?
CG-Only: Wide DRAM channel
FG-Only: Many narrow channels

## Slide 92
Coarse- or fine-grained memory access?
D0
E0
Data
C
C0
C1
D1
E1
D2
E2
D3
E3
C2
C3
C4
D4
E4
CG
FG
C5
C6
C7
D5
E5
D6
E6
D7
E7
ECC
D0
E0
Data
C
C0
CG
FG
ECC

## Slide 93: Dynamically adapt granularity  best of both worlds
Processor
Core
$I
$D
L2
Last Level Cache
MC
DRAM
Core
0
Core
1
Core
N-1
…
SLP
Co-scheduling CG/FG w/ split CG
Sector cache
(8 8B sectors per line)
Sub-Ranked DRAM w/ 2X ABUS
Support both CG and FG
Locality Predictor

## Slide 94
Subranked memory
  Adapt parallelism
DBUS
x8
x8
x8
x8
x8
x8
x8
x8
x8
ABUS
SR0
SR1
SR2
SR3
SR4
SR5
SR6
SR7
SR8
Reg/Demux

## Slide 95
Sectored caches
  Track granularity
tag
sector 0
D
V
sector 1
D
V
sector 2
D
V
sector 3
D
V
tag
data
D
V
Long cache line
Sector cache
tag
data
D
V
Short cache line

## Slide 96
Granularity information?
  Application provided (when allocated)
  System learned (when accessed)

## Slide 97
Chart: System Throughput
| mcf x8 | omnetpp x8 | mst x8 | em3d x8 | canneal x8 | SSCA2 x8 | linked list x8 | gups x8 | MIX-A | MIX-B | MIX-C | MIX-D
CG | 1.2651 | 2.0696 | 1.9539 | 1.524 | 1.7956 | 0.90264 | 2.5045 | 1.2143 | 1.6595 | 1.5276 | 2.6008 | 3.1503
FG+ECC | 1.5782 | 2.8463 | 3.5473 | 2.4007 | 4.3254 | 1.5027 | 7.0961 | 3.4946 | 2.1429 | 2.2023 | 2.2747 | 2.6085
AG+ECC | 1.5782 | 2.9049 | 4.0292 | 2.8944 | 4.3317 | 1.6105 | 7.2252 | 4.0714 | 2.1725 | 2.2749 | 3.0385 | 3.6587
CG+ECC
FG+ECC
AG+ECC
Dynamically adapt granularity
PROPORTIONALITY

## Slide 98
Memory is heterogeneous
Applications are heterogeneous
this is a good thing

## Slide 99
Adaptivity is key

## Slide 100
Sometimes need application help
  Programming models and analyses crucial

## Slide 101
Think abstractions rather than examples

## Slide 102
Memory is heterogeneous
Applications are heterogeneous
this is a good thing
Adaptivity is key
Sometimes need application help
  Programming models and analyses crucial
Think abstractions rather than examples