## Slide 1: Toward Exascale Resilience Part 1: Overview of challenges and trends
Mattan Erez
The University of Texas at Austin
July 2015

## Slide 2
With support from
  DOE
  NSF

## Slide 3
Bottom line:
System Complexity increasing
faster than
component reliability improves
No “right” answer
Notes: Overview of extreme scale resilience and trends
System architecture and components (hardware and software)
Taxonomy of reliability and resilience
Detection -> Containment -> Repair
Forward and backward recovery
Fault modes and models
Error models and Failure models
Memory and networks
Past, present, and near future approaches
Checkpoint restart (classic and improvements)
Impact of level of paranoia
Why supercomputers aren't clouds and what can be learned
Hardware techniques
Containment domains and other Cross-level approaches

## Slide 4
An exascale system is a high-performance system for solving big problems

## Slide 5
An exascale system is a high-performance system for solving big cohesive problems

## Slide 6
An exascale system is a high-performance system for solving big cohesive problems
Notes: 1

## Slide 7
An exascale system is a high-performance system for solving big cohesive problems

## Slide 8
Complexity and components

## Slide 9
Performance outpaces even idealized VLSI
  HW component count increases exponentially
Chart: Sustained FLOP/s
| 1993 | 1994 | 1994 | 1995 | 1995 | 1996 | 1996 | 1997 | 1997 | 1998 | 1998 | 1999 | 1999 | 2000 | 2000 | 2001 | 2001 | 2002 | 2002 | 2003 | 2003 | 2004 | 2004 | 2005 | 2005 | 2006 | 2006 | 2007 | 2007 | 2008 | 2008 | 2009 | 2009 | 2010 | 2010 | 2011 | 2011 | 2012 | 2012 | 2013 | 2013 | 2014 | 2014 | 2015 | 2015 | 2016 | 2016 | 2017 | 2017 | 2018 | 2018
Num. 1 | 124000000000 | 124000000000 | 196000000000 | 196000000000 | 196000000000 | 232400000000 | 368200000000 | 1068000000000 | 1338000000000 | 1338000000000 | 1338000000000 | 2121000000000 | 2379000000000 | 2379000000000 | 7304000000000 | 7304000000000 | 7304000000000 | 35860000000000 | 35860000000000 | 35860000000000 | 35860000000000 | 35860000000000 | 70720000000000 | 136800000000000 | 280600000000000 | 280600000000000 | 280600000000000 | 280600000000000 | 280600000000000 | 1026000000000000 | 1105000000000000 | 1105000000000000 | 1759000000000000 | 1759000000000000 | 2566000000000000 | 8162000000000000 | 10150000000000000 | 16320000000000000 | 17590000000000000 | 33862700000000000 | 45150266666666664 | 60200355555555552 | 80267140740740736 | 1.0702e+17 | 1.427e+17 | 1.9026e+17 | 2.5368e+17 | 3.3825e+17 | 4.5099e+17 | 6.0132e+17 | 8.0177e+17
Num. 10 | 15100000000 | 27500000000 | 27500000000 | 51000000000 | 59700000000 | 67000000000 | 94300000000 | 176000000000 | 196000000000 | 321000000000 | 448600000000 | 509000000000 | 558000000000 | 815000000000 | 892000000000 | 1179000000000 | 1293000000000 | 2050000000000 | 3164000000000 | 3980000000000 | 6586000000000 | 8061000000000 | 9819000000000 | 15250000000000 | 20530000000000 | 35680000000000 | 43480000000000 | 56520000000000 | 82160000000000 | 106100000000000 | 204000000000000 | 274000000000000 | 423000000000000 | 433500000000000 | 816000000000000 | 1042000000000000 | 1042000000000000 | 1271000000000000 | 1515000000000000 | 2566000000000000 | 3167901234567901 | 3910989178478890 | 4828381701825790 | 5960965063982456 | 7359216128373402 | 9085452010337532 | 11216607420169792 | 13847663481691100 | 17095880841593950 | 21106025730362900 | 26056821889336912
Num.500 | 470000000 | 820000000 | 1100000000 | 2000000000 | 2500000000 | 3300000000 | 4600000000 | 7700000000 | 9500000000 | 13400000000 | 17100000000 | 25000000000 | 33100000000 | 44000000000 | 55300000000 | 67800000000 | 94300000000 | 134300000000 | 191800000000 | 245000000000 | 402000000000 | 624000000000 | 851000000000 | 1170000000000 | 1650000000000 | 2030000000000 | 2740000000000 | 4010000000000 | 5930000000000 | 17860000000000 | 12600000000000 | 17100000000000 | 20700000000000 | 24670000000000 | 31240000000000 | 40870000000000 | 50940000000000 | 60824000000000 | 76140000000000 | 96619000000000 | 1.1928e+14 | 1.4726e+14 | 1.8181e+14 | 2.2445e+14 | 2.771e+14 | 3.421e+14 | 4.2235e+14 | 5.2141e+14 | 6.4372e+14 | 7.9472e+14 | 9.8113e+14
Idealized VLSI | 73703703703.7037 | 90992226794.6959 | 112336082462.5876 | 138686521558.7501 | 171217927850.3087 | 211380157839.8873 | 260963157827.0213 | 322176738058.051 | 397749059330.9272 | 491048221396.2064 | 606232372094.0819 | 748435027276.6443 | 923993860835.3633 | 1.1407e+12 | 1.4083e+12 | 1.7387e+12 | 2.1465e+12 | 2.65e+12 | 3.2716e+12 | 4.039e+12 | 4.9864e+12 | 6.1561e+12 | 7.6001e+12 | 9.3828e+12 | 1.1584e+13 | 1.4301e+13 | 1.7655e+13 | 2.1797e+13 | 2.691e+13 | 3.3222e+13 | 4.1015e+13 | 5.0635e+13 | 6.2513e+13 | 7.7176e+13 | 9.5279e+13 | 117628795922846 | 1.4522e+14 | 1.7928e+14 | 2.2134e+14 | 2.7326e+14 | 3.3736e+14 | 4.1649e+14 | 5.1418e+14 | 634795004558102 | 7.837e+14 | 9.6753e+14 | 1194478793616040 | 1474665177303753 | 1.8206e+15 | 2.2476e+15 | 2774842696185941
top500.org + extrapolation
Notes: Performance keeps marching on
Outpaces idealized technology
Technology not keeping up with ideal

## Slide 10
Logic
Memory
Links
Power
Cooling

## Slide 11
SW growing too
  HW controlled by complex and sophisticated SW
From Linux Foundation

## Slide 12
Management SW
Node OS
Application runtime
Application

## Slide 13
What about component reliability?

## Slide 14
Reliable == runs without failing
  Failure means result is out of specification scope
  Reliability is hierarchical – reliable systems from unreliable components
Fault
Error
Failure
cause of failure
component departs from spec.
service departs from spec.
open/short circuit
transistor wear-out
particle strike
…
Wrong value
Wrong control
Application result incorrect
Transient / non-transient fault
Error tolerance
Notes: Here are some terminologies that I will use throughout the presentation.
A fault is an underlying cause of failure. In DRAM, it can be something like an alpha-particle strike.
Due to a fault, a component may depart from its expected behavior, which we call an error. In our research of ECC memory, error indicates incorrect read data.
A failure happens when service departs from its spec. In our research, it happens when memory returns incorrect data to processor.
In more details,
A transient fault manifests error once, while a non-transient fault manifests multiple times.
And the goal of ECC is to stop failure manifestation by detecting and correcting errors.

## Slide 15
What about component reliability?
  Significant uncertainty about predictions
  Largely because technology doesn’t stand still

## Slide 16
An alarmist extrapolation
  Also with significant silent data corruption concern
Chart: Year (Expected performance in PetaFlops)
| 2013 (15PF) | 2015 (40PF) | 2017 (130PF) | 2019 (450PF) | 2021 (1500PF)
Hard | 13.3333 | 8.658 | 5.6221 | 3.6507 | 2.3706
Soft | 200 | 60.6061 | 18.3655 | 5.5653 | 1.6865
Intermittent SW | 16.6667 | 12.6263 | 9.5654 | 7.2465 | 5.4898
Overall | 7.1429 | 4.7348 | 2.9686 | 1.6903 | 0.83545

## Slide 17
Vendors work hard to keep reliability constant
  Reliability doesn’t come cheap though

## Slide 18
VLSI exponentials result from discrete steps
From Mark Bohr, Intel (“Moore’s Law: Yesterday, Today, and Tomorrow”, May 26, 2015

## Slide 19
An optimistic projection
  SDC concerns les clear
Chart: Year (Expected performance in PetaFlops)
| 2013 (15PF) | 2015 (40PF) | 2017 (130PF) | 2019 (450PF) | 2021 (1500PF)
Hard | 10.5263 | 8.6994 | 7.1896 | 5.9418 | 4.9106
Soft | 80 | 60.6061 | 45.9137 | 34.7831 | 26.3508
Intermittent SW | 16.6667 | 12.6263 | 9.5654 | 7.2465 | 5.4898
Overall | 5.9701 | 4.7472 | 3.7677 | 2.9847 | 2.3599

## Slide 20
Can all vendors succeed?
  At what cost?

## Slide 21
Do all customers care?
  “Commercial” vs. scientific
  Clouds vs. supercomputers
  Games vs. supercomputers

## Slide 22
The cohesiveness problem
  Performance efficiency is expected performance relative to perfectly-reliable system
Chart: Performance Efficiency
| 2013 (15PF) | 2015 (40PF) | 2017 (130PF) | 2019 (450PF) | 2021 (1500PF)
Cohesive Alarmist | 0.94515 | 0.91812 | 0.8718 | 0.78308 | 0.59807
Cohesive Optimistic | 0.93464 | 0.91833 | 0.89792 | 0.87246 | 0.84077
Independent | 1 | 1 | 1 | 1 | 1

## Slide 23
Reliability is in the eye of the beholder
  Level of paranoia (life threatening?)
  Monetary cost of failure (and legal implications)
  Tolerance to different results
  Can someone else be blamed?

## Slide 24
No “right answer”
  Performance/efficiency and reliability tradeoffs

## Slide 25
Short course goals
  For hardware, system, and application:
    Understand the state of the practice
    Understand the state of the art
    Understand the sources of overhead
    Understand how to improve resilience within a layer
  Understand cross-layer resilience
    Better balance of overheads and needs

## Slide 26
Syllabus (basics, then bottom-up)
  Overall system architecture
  Fundamentals of resilience
    Terminology and actions
  Fault/error/failure modes and models
  Past, present, and near future approaches
    HW techniques + checkpoint/restart
  Supercomputers aren’t clouds
    But what can we learn?
  Containment Domains and other future cross-layer approaches
    With thoughts on approximate computing
  Reporting and forecasting

## Slide 27: An aside about mE

## Slide 28: Big problems and emerging systems
Resilience/ Reliability
Het. Proc. / supercomputing / cloud
Memory

## Slide 29: Arch-focused whole-system approach
Efficiency requirements require crossing layers
Algorithms are key
  Compute less, move less, store less
Proportional systems
  Minimize waste
Utilize and improve emerging technologies
Explore (and act) up and down
  Programming model to circuits
Preferably implement at micro-arch/system

## Slide 30: Big problems and emerging platforms
Memory systems
  Capacity, bandwidth, efficiency – impossible to balance
  Adaptive and dynamic management helps
  New technologies to the rescue?
  Opportunities for in-memory computing
GPUs, supercomputers, clouds, and more
  Throughput oriented designs are a must
  Centralization trend is interesting
Reliability and resilience
  More, smaller devices – danger of poor reliability
  Trimmed margins – less room for error
  Hard constraints – efficiency is a must
  Scale exacerbates reliability and resilience concerns

## Slide 31
Current and graduated PhD students
  Benjamin Cho
  Jinsuk Chung
  Seong-Lyong Gong
  Cagri Eryilmaz
  Dong Wan Kim
  Jungrae Kim
  Evgeni Krimer (NVIDIA)
  Min Kyu Jeong (Oracle Labs)
  Ikhwan Lee
  Kyushick Lee
  Mike Sullivan (NVIDIA Research)
  Minsoo Rhu (NVIDIA Research)
  Doe Hyun Yoon (Google)
  Song Zhang
  Tianhao Zheng
  Haishan Zhu
Current and graduate MS students
  Mehmet Basoglu (Broadcom)
  Esha Choukse
  Nick Kelly
  Mahnaz Sadoughi (Apple)
Collaborators at
  AMD
  Cray
  Intel
  NVIDIA
  Samsung
  LBNL, PNNL
  Stanford
Lots of great insightful feedback

## Slide 32
Grew up mostly in Israel
BSc EE and BS Physics at Technion
Part-time researcher at Intel Haifa
PhD at Stanford (w/ Bill Dally)
At UT Austin since 2007
  Going well (great students and collaborators)
  ~7 architects + ~5 systems
  Very strong collaborations with others
  TACC supercomputing center