## Slide 1: Toward Exascale Resilience Part 2: System Architecture and Components Resilience fundamentals
Mattan Erez
The University of Texas at Austin
July 2015

## Slide 2
Algorithm
Program
Runtime
Operating system
Compiler
HW Architecture
HW Devices
Resilience
Reliability

## Slide 3
A concentrated exaflop
  Cohesive system for cohesive problems

## Slide 4
From a Cray XC30

## Slide 5
Hardware summary
  Cabinets (w/ VRU)
  Shared power, cooling, and links (w/ VRU)
  Modules (w/ VRU)
  Sockets
  Processors + memories
  Gates, wires, and storage devices
  Storage separated out (for now)

## Slide 6
System software manages resources
  Node operating system
  Distributed file system and I/O nodes
  System management and supervision

## Slide 7: Resilience fundamentals
Terminology
Principles
Basic actions

## Slide 8
Faults, errors, and failures
Fault
Error
Failure
cause of failure
component departs from spec.
service departs from spec.
open/short circuit
transistor wear-out
particle strike
…
Wrong value
Wrong control
Application result incorrect

## Slide 9
Fault taxonomy (others exist)
  What?
    Component malfunction
    May lead to errors
  Where?
    What component? Hardware or software?
  How?
    Natural / accidental / intentional?
  When?
    Permanent / transient
    Active / dormant
    Reproducible / random
    0-day?

## Slide 10
When do we care about faults?

## Slide 11
Error taxonomy
  What?
    State that differs from fault free state
  Where?
    Values or control state
  How?
    Data dependent / independent
  When?
    Permanent / transient / intermittent
    Reproducible / random
  Impact?
    Masked / detected / silent

## Slide 12
Failure taxonomy
  What?
    Actionable outputs not within spec
    Performance / power not within spec degraded operation
  Where?
    Can be hierarchical to a subsystem
  When?
    Signaled / silent
    Failstop / failthrough
    Consistent / inconsistent

## Slide 13
Resilience = operating without failure in the presence of faults and errors
  Fault tolerance
  Fault mitigation
  Fault avoidance
  Error tolerance
  Error mitigation

## Slide 14
(Forecast)
Detect
Contain
Recover
Repair

## Slide 15
Fault/failure forecast
  Use past experience to forecast future problems
  Avoid faults and failures
    Reconfiguration
    Preventative-repair
  Traditionally done offline
    Stress diagnostics
  Online work looks promising
    Mostly machine learning approaches
  Requires effective monitoring

## Slide 16
Detection
  Diagnostics for faults
  Redundancy for errors
    Redundancy may be implicit
  Detected errors may identify faults
    Root-cause analysis
  Requires effective reporting

## Slide 17
Containment
  Error propagation increases costs
    More to mitigate
    More likely to lead to a failure
  Containment enables resilience
  Careful design
  Timely reporting

## Slide 18
Recover (error mitigation)
  Forward recovery (masking)
    Requires redundancy
    Some errors ignorable
  Backward recovery (re-execution)
    Requires preserved state

## Slide 19
Repair (fault mitigation)
  Reconfigure to degraded operation
  Replace with hot spare
  Replace with cold spare
  Fix
    Usually for software

## Slide 20
Metrics
  Why measure
  Who is measuring

## Slide 21
If you cannot measure it, you cannot improve it Lord Kelvin

## Slide 22
FIT – the unit of resilience and reliability
Generic “faults in time”
1 FIT  1 fault in 109 hours of operation
  Really annoying unit
  But, rates accumulate

## Slide 23
What do users care about?

## Slide 24
What do users care about?
  Time to completion
  Cost of computation
  Correctness of answer
  Are they part of the solution

## Slide 25
Relative efficiency
  Performance, power, time, energy, … with resilience relative to assuming perfectly-reliable system
  How much are overhead is a user paying for a particular resilience scheme
  Setting baseline in reality is tricky
    Differences between components

## Slide 26
Relative correctness
  Bit-by-bit perfect
  Same printout
  Matches expectations
    Need to quantify expectations

## Slide 27
Relative effort
  How much is required from the user?
  Users are accustomed to reliable systems
  Users always resist change
  How often are they interrupted

## Slide 28
What about systems people?

## Slide 29
What about systems people?
  Underlying system failure characteristics
  Availability
    Overall / “Scheduled”
  *MTTI (mean time to interrupt)
  *MTBI (mean time between interrupts)
  *MTTR (mean time to repair)
  * =
    System, application, job, node, …
Unscheduled donwtime