## Slide 1: Toward Exascale Resilience Part 3: Fault and error modes and models
Mattan Erez
The University of Texas at Austin
July 2015

## Slide 2
Why care about models?

## Slide 3
Why care about models?
  Resilience isn’t free
  Paying too much overhead means losing out

## Slide 4
Modeling techniques
  “First-principles” (simulation and analytical)
    How detailed?
    What parameters?
  Empirical
    Accelerated testing
    Field studies
  Extrapolations

## Slide 5
Different components – different techniques
  Academic are not in the best position here

## Slide 6
Field studies
  Collect fault, error, failure reports from actual systems
  Analyze
  Draw conclusions
  Extrapolate

## Slide 7
Field studies are hard
  Limited reporting
  Limited information
  Limited access
  Sensitive outcomes
But, that’s the actual world

## Slide 8
Some excellent examples in recent years
  In particular for DRAM
    Starting from Sridharan and Liberty, SC’12
  Good sources for other components too
    Recent analysis on supercomputers and datacenters
    Some other specific components too

## Slide 9
Fault vs. error/failure analysis

## Slide 10
Accelerated testing
  Baking
  Beam testing
Excellent, but
  Special facilities
  Special equipment

## Slide 11
Back to basics

## Slide 12
Hard faults and intermittent errors
  Design flaws
  Fabrication defects
  Process variation
  Mechanical stress
  Gradual wearout
Soft faults
  Alpha particles
  Cosmic rays
  Power supply variation
  Voltage droops
  Crosstalk

## Slide 13
Hardware summary
  Gates, wires, and memory devices
  Memories and processors (sockets)
  Modules (w/ VRU)
  Shared power, cooling, and links (w/ VRU)
  Cabinets (w/ VRU)
  Storage separated out (for now)

## Slide 14
Hard faults in processors
  Manufacturing
  Mechanical
  Wearout
Industry probably has these under control
  ALL customers need this to work
  Several recent studies suggest it is indeed the case

## Slide 15
But not clear what is sacrificed
  How much better could we do if system exposed to processor hard faults?

## Slide 16
Example: gradual wearout

## Slide 17
Particle-strike soft errors
  Ionizing particle frees electron-hole pairs in transistor active region
  Charge collected at source/drain creating current in an off device
  Current can flip a bit in a storage device or change value of a logic computation

## Slide 18
Why are particle strikes problematic?
  Two main sources
    Alpha particles
    Atmospheric neutrons
  Alpha particles from packaging and solder
    Can be reduced but not eliminated completely
  Neutrons are highly penetrating and flux can be high
    Neutrons randomly strike an atom and create secondary ionizing particles
Difficult to stop, but rare
  Protection overhead is high and generally “wasted”
  Minimize waste by understanding vulnerability and trends
Need models for:
  Particle flux, charge collection, and component vulnerability

## Slide 19: Likelihood of Strike Directly Proportional to Particle Flux
Alpha particles are low and constant flux
Neutrons more interesting and problematic
Significant number of high-energy neutrons
Even higher flux at lower energies
  Lower energies may affect future technologies more

## Slide 20: Flux Varies Significantly with Altitude and Latitude
Flux at 50,000’ is 1000 times higher than at sea level
Flux towards poles 5 times higher than equator

## Slide 21: Impact of a Particle Strike
Amount of freed charge
  Energy of particle (nature)
  Angle of incidence (generally random)
  Properties of material (hard to gauge)
Efficiency of charge collection
  Volume of depletion zone (shrinks with tech. scaling)
  Supply voltage (small linear impact)
  Temperature (minimal impact)
Required current/charge to cause an error
  Qcrit is minimal charge to flip an SRAM bit
  Similar notion for latches
  More complex for logic

## Slide 22: SRAM Trends
Qcrit decreases with technology scaling
  Lower capacitance to overcome for a flip (linear)
  Lower voltage lowers Qcrit (linear and small)
Collected charge also decreases somewhat
Process variation increases error propensity
  Variation increases as technology scales
New transistor technology reduces error propensity
  Also helps limit variation
FIT per bit expected roughly constant
Denser devices increase number of bits and also likelihood of multi-bit upsets

## Slide 23: SRAM Trends
Multi-bit errors significant concern

## Slide 24: Latch Trends
Similar to SRAM
Fewer bits, but large enough to be a problem
Mitigation techniques differ
  Latches often synthesized rather than in arrays
  Hardened latches are common, but expensive, solution
MBUs also a problem
  Accesses mostly narrow

## Slide 25: Logic Trends
Particle strike to off transistor “turns” it on
Charge translates to current pulse
  Current flows as long as charge being collected
Current pulse may not result in an error
  Logical masking (unaffected by scaling)
  Temporal masking (related to frequency, expected fixed)
  Electrical masking
    Decreases with scale
    Mitigation possible with minimal “hardening”
Overall expected 0.5% SER compared to SRAM/latch

## Slide 26: Other soft faults
Shrinking margins and growing variations 
can lead to timing violations
Our research matches results from IBM research:
  Gain is ~20%
  Almost all this gain possible with reasonable (though dynamic) margins

## Slide 27
But what about errors?
  Logic faults/errors very frequently masked
  Error disappears before being latched (timing)
  Error diminishes and disappears because of signal rectification (electrical masking)
  Values lead to logical masking

## Slide 28
Error modeling?
  Logic simulation
  Multi-mode simulation

## Slide 29
Quick(ish) way to search the error space
  Multi-mode simulation
  Skip over detectable errors
  Tool to be released
    Uses only public tools

## Slide 30
DRAM faults very problematic
  Dozens of DRAM chips per processor
  Millions per system
  New DRAM fault every couple of hours
  Modules are expensive

## Slide 31
Memory must be reliable
  Written data must be recalled “correctly”

## Slide 32
Reliability challenges
  “Natural” change in cell value
  Induced change in cell value
  Read errors
  Write errors
  Wearout and defects

## Slide 33
Natural causes of value change
Probability correct
Time
Decay
  Refresh
Notes: Natural change in state
  Decay
    DRAM leakage (refresh)
    PCM, Memristor, RRAM drift
  Flips
    DRAM/SRAM/latch particle strikes
    STT MRAM state flips
  Control
    Control-related soft errors corrupt values

## Slide 34
Natural causes of value change
Probability correct
Time
Probability correct
Time
Decay
  Refresh
Flip
  ECC + scrub
Notes: Natural change in state
  Decay
    DRAM leakage (refresh)
    PCM, Memristor, RRAM drift
  Flips
    DRAM/SRAM/latch particle strikes
    STT MRAM state flips
  Control
    Control-related soft errors corrupt values

## Slide 35
Natural causes of value change
Probability correct
Time
Probability correct
Time
Decay
  Refresh / scrub
Flip
  ECC + scrub

## Slide 36
Natural causes of value change
Probability correct
Time
Probability correct
Time
  Retention control
    Less dense
    Writes slower/higher-energy
    Can use different devices
Decay
  Refresh / scrub
Flip
  ECC + scrub
Notes: Natural change in state
  Decay
    DRAM leakage (refresh)
    PCM, Memristor, RRAM drift
  Flips
    DRAM/SRAM/latch particle strikes
    STT MRAM state flips
  Control
    Control-related soft errors corrupt values

## Slide 37
Induced change in value
  Writing or reading disturbs nearby cells
  Worse for writes
  Technology and design dependent

## Slide 38
Read errors
  Because of small margins for efficiency

## Slide 39
Write errors
  Writing implies changing a state or value
  Stochastic
Probability correct
Time

## Slide 40
Write errors
  Writing implies changing a state or value
  Stochastic
  Waiting inefficient and slow
  Write error control conflicts w/ other errors
Probability correct
Time

## Slide 41
Wearout and defects
Probability correct
Time
Probability correct
Time
Probability correct
Time
Probability correct
Time

## Slide 42
Wearout and defects
  Sparing
  Extra margins
  Retirement
  Compensation (ECC)

## Slide 43
Summary: no “good” memory
  It’s all about tradeoffs

## Slide 44
But, those tradeoffs barely up to us
  Good empirical models for DRAM
  So far, vendors maintaining targets
Interestingly, peripheral circuits very vulnerable

## Slide 45: But at the end, good empirical models exist and are currently maintained
Rules of thumb (more later)
  50/50 soft/hard
  50/50 single/multi bit
Mat
Notes: Our 3rd and final observation is from DRAM internal structure.
If we have a closer look to DRAM, each bank is partitioned into sub-structures called mats.
And for routing efficiency, data within a Mat go to the same data pin (DQ).
As a result, if a local fault generates multiple errors on a mat, it will affect only a single data pin over multiple burst beats, as shown in the figure.

## Slide 46
DRAM Errors?
  Highly dependent on ECC scheme
  Probably pretty random

## Slide 47
Other hard faults
  Corrosion
  Mechanical stress
  Accidents
  Current stress
Mechanical  power  connectors
  Lots of redundancy can be put in
  Recently, scaling in the chip faster than outside

## Slide 48
Network
  Processor + memory + links
  Few models available
  Generally very resilient
    Strong error protection
    Routing adapts to hard faults

## Slide 49
An example: Blue Waters
From Di Marino et al., DSN’14

## Slide 50
An example: Blue Waters
From Di Marino et al., DSN’14

## Slide 51
An example: Blue Waters
From Di Marino et al., DSN’14