## Slide 1: Toward Exascale Resilience Part 8: Containment Domains / cross-layer schemes
Mattan Erez
The University of Texas at Austin
July 2015

## Slide 2
Credit to:
UT Austin students:
  Benjaming Cho, Jinsuk Chung, Ali Fakhrzadehgan, Ikhwan Lee, Kyushick Lee, Seong-Lyong Gong, Mike Sullivan, Song Zhang, Doe Hyun Yoon (now at Google)
Collaborators (growing list)
  Cray, NVIDIA, ETI
  LBNL: Brian Austin, Dan Bonachea, Paul Hargrove , Sherry Li, Eric Roman
Funding agencies
  DOE ECRP, XStack, FF, PSAAP II
  Initial funding from DARPA UHPC

## Slide 3
The constraints:
  Power/energy
  Time
  Money
  Correctness

## Slide 4
Resilience is a big challenge for DOE computations

## Slide 5
Something bad every ~minute at DOE scale
Chart: Year (Expected performance in PetaFlops)
| 2013 (15PF) | 2015 (40PF) | 2017 (130PF) | 2019 (450PF) | 2021 (1500PF)
Hard | 16.6667 | 12.6263 | 9.5654 | 7.2465 | 5.4898
Soft | 400 | 121.2121 | 36.7309 | 11.1306 | 3.3729
Intermittent SW | 28.5714 | 18.5529 | 12.0473 | 7.8229 | 5.0798
Overall | 10.2564 | 7.0746 | 4.656 | 2.8116 | 1.4804

## Slide 6
The baseline: checkpoint-restart
Not good enough on its own

## Slide 7
Failure rate too high for checkpoint/restart
Correctness also at risk
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.99175 | 0.98422 | 0.98302 | 0.97237 | 0.96043 | 0.94702 | 0.9429
h-CPR, 80% | 0.98845 | 0.98064 | 0.96938 | 0.94865 | 0.90855 | 0.85606 | 0.81179
g-CPR, 80% | 0.90834 | 0.80169 | 0.58706 | 0.17499 | 0 | 0 | 0

## Slide 8
Energy also problematic
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.0063317 | 0.0087139 | 0.011899 | 0.01684 | 0.031066 | 0.034466 | 0.03948
h-CPR, 80% | 0.011686 | 0.019745 | 0.031588 | 0.054126 | 0.10065 | 0.16815 | 0.23184
gCPR, 80% | 0.10092 | 0.24736 | 0.70342 | 4.7145 | 0 | 0 | 0

## Slide 9
The cost of resilience
  Preparation
  Detection
  Mitigation (repair + recover)
  Implementation

## Slide 10
Software?
Hardware?
Algorithm?

## Slide 11
Software?
Hardware?
Algorithm?
Containment Domains: adaptive holistic approach
  Per-experiment balance of energy, time, money, correctness

## Slide 12
Can hardware alone solve the problem?
Yes, but costly
  Significant and likely fixed overheads
  May not be needed in many commercial settings

## Slide 13
Fixed overhead examples (estimated) Both energy and/or throughput
  Up to ~25% chipkill correct vs. chipkill detect
  20 – 40% for pipeline SDC reduction
  >2X for arbitrary correction
  Even greater overhead if protecting approximate units

## Slide 14
Something bad every ~minute at DOE
Something bad every year commercially
  Smaller units of execution
  Different requirements

## Slide 15
Locality and hierarchy are key
  Hierarchical constructs
  Distributed operation
Range of correctness requirements

## Slide 16
What about algorithmic resilience?
  Algorithmic detection
  Iterative converging algorithms
  Redundant information
  Probabilistic methods

## Slide 17
Examples on board
  Algorithmic check of matrix multiplication
  Algorithmic check of a solver
  Convergent calculation
    Simple and basic Newton-Raphson
  Monte Carlo

## Slide 18
But,
Different apps  different techniques Different scales  different techniques

## Slide 19
Need to adapt/co-tune

## Slide 20
Containment Domains elevate resilience to first-class abstraction
  Program-structure abstractions
  Composable resilient program components
  Regimented development flow
  Supporting tools and mechanisms

## Slide 21
Containment Domains
  Abstract resilience constructs that span system layers
  Hierarchical and Distributed operation for locality
  Scalable to large systems with high energy efficiency
  Heterogeneous to match disparate error/failure effects
  Proportional and effectively balanced
  Tunable resilience specialized to application/system
  Analyzable and auto-tuned

## Slide 22: CDs Embed Resilience within Application
Express resilience as a tree of CDs
  Match CD, task, and machine hierarchies
  Escalation for differentiated error handling
Semantics
  Erroneous data never communicated
  Each CD provides recovery mechanism
Components of a CD
  Preserve data on domain start
  Compute (domain body)
  Detect faults before domain commits
  Recover from detected errors
Root CD
Child CD

## Slide 23: Mapping example: SpMV
Matrix M
Vector V
void task<inner> SpMV(in M, in Vi, out Ri) {
cd = GetCurrentCD() ->CreateAndBegin();
cd->Preserve(matrix, size, kCopy);
forall(…) reduce(…) SpMV(M[…],Vi[…],Ri[…]);
cd->Complete();
}
void task<leaf> SpMV(…) {
cd = GetCurrentCD() ->CreateAndBegin();
cd->Preserve(M, sizeof(M), kRef); cd->Preserve(Vi, sizeof(Vi), kCopy); for r=0..N
for c=rowS[r]..rowS[r+1] resi[r]+=data[c]*Vi[cIdx[c]];
cd->CDAssert(idx > prevIdx, kSoft);
prevC=c;
cd->Complete();
}

## Slide 24: Mapping example: SpMV
Matrix M
Vector V
void task<inner> SpMV(in M, in Vi, out Ri) {
cd = GetCurrentCD() ->CreateAndBegin();
cd->Preserve(matrix, size, kCopy);
forall(…) reduce(…) SpMV(M[…],Vi[…],Ri[…]);
cd->Complete();
}
void task<leaf> SpMV(…) {
cd = GetCurrentCD() ->CreateAndBegin();
cd->Preserve(M, sizeof(M), kRef); cd->Preserve(Vi, sizeof(Vi), kCopy); for r=0..N
for c=rowS[r]..rowS[r+1] resi[r]+=data[c]*Vi[cIdx[c]];
cd->CDAssert(idx > prevIdx, kSoft);
prevC=c;
cd->Complete();
}

## Slide 25: Mapping example: SpMV
Matrix M
Vector V
Distributed to 4 nodes
void task<leaf> SpMV(…) {
cd = GetCurrentCD() ->CreateAndBegin();
cd->Preserve(M, sizeof(M), kRef); cd->Preserve(Vi, sizeof(Vi), kCopy); for r=0..N
for c=rowS[r]..rowS[r+1] resi[r]+=data[c]*Vi[cIdx[c]];
cd->CDAssert(idx > prevIdx, kSoft);
prevC=c;
cd->Complete();
}

## Slide 26: Mapping example: SpMV
Matrix M
Vector V
Distributed to 4 nodes
void task<leaf> SpMV(…) {
cd = GetCurrentCD() ->CreateAndBegin();
cd->Preserve(M, sizeof(M), kRef); cd->Preserve(Vi, sizeof(Vi), kCopy); for r=0..N
for c=rowS[r]..rowS[r+1] resi[r]+=data[c]*Vi[cIdx[c]];
cd->CDAssert(idx > prevIdx, kSoft);
prevC=c;
cd->Complete();
}

## Slide 27: Concise abstraction for complex behavior
Local copy or regen
Sibling
Parent (unchanged)
void task<leaf> SpMV(…) {
cd = GetCurrentCD() ->CreateAndBegin();
cd->Preserve(M, sizeof(M), kRef); cd->Preserve(Vi, sizeof(Vi), kCopy); for r=0..N
for c=rowS[r]..rowS[r+1] resi[r]+=data[c]*Vi[cIdx[c]];
cd->CDAssert(idx > prevIdx, kSoft);
prevC=c;
cd->Complete();
}

## Slide 28
Programming and execution model support

## Slide 29
CDs manage preservation, restoration, and re-execution
  Allocate and frees storage
  Transfer data
  Manage default error detection
  Call appropriate CD (hierarchy level) on error/fault
  Holistic error reporting
Specific policies can be written by the user
  Specialize and tune every aspect of resilience
  Straightforward abstractions
CD abstraction amenable to analysis and auto-tuning
  Analytical model fed with application properties
Notes: ##Single Consistent abstraction##
1. One of the key aspects of containment domains are that they are single consistent abstraction.
2. Abstractions enable us to capture existing resilience techniques.
3. You can have a consistent way of expressing resilience concerns from application through analysis down to system implementation.
##Components##
4. To achieve that we express a program with a hierarchy of containment domains. Each containment domains has four components.
##Semantics##
5. In addition to four components, we require each containment domain to obey two simple semantics.
6. Errorneous data is never communicated out side of a containment domain.
7. Each containment domain provides some mechanism for recovery. It could be reexecution, re-generation of the data, or potentially because we have hierarchy of containment domains, some errors may not be efficiently tolerated in a certain containment domain level and instead the error can be escalated. If everything escalates all the way to the root it essentially matches global check point restart.
-------------------------------
Containment domain is a single consistent abstraction that encapsulates resilience concerns.
In addition to four components, we require each containment domain to obey two simple semantics.
No erroneous data is consumed by other domains.
Second, is that each cd provides
Recovery could be escalation.
If the overhead of handling the error at this level is too high, it gets escalated.
During the mapping, which error is handled at a level is decided.
Hierarchy and containment is key enabling mechanisms for handling errors efficiently. Also for simplifying the analysis.
--------------------------------------------------
Main points: Containment Domains encapsulates existing techniques + Erroneous data never communicated + Hierarchy
-> This makes analysis easy
-> Also makes error handled hierarchical -> thus efficient
If the overhead of handling the error at this level is too high, it gets escalated.
During the mapping -> which error is handled is decided -> if overhead is too high make them escalate.

## Slide 30
  Annotations, persistence, reporting, recovery, tools
CD-annotated Applications/Libraries
CD Runtime System
Hardware
Compiler Support
Debugger
CD-App
Mapper
User Interaction for customized error
detection /handling / tolerance / injection
Auto-tuner
Interface
Profiling & Visualization Interface
CD
Auto Tuner
Sight
Scaling Tool
(LWM2)
Error
Handling
Unified Runtime Error Detector
Persistence Layer
State Preservation
Communication Logging
Runtime Logging
Communication Runtime Library
(Legion + GasNet)
Legion + Libc
BLCR
CD-Storage
Mapping Interface
Low-Level Machine Check HW/SW I/F
Error Reporting Architecture
PFS
Buddy
DRAM
SSD
HDD
External Tool
Internal Tool
Future Plan
CD Runtime System Architecture

## Slide 31
CD usage flow
  Annotate
  Profile and extrapolate CD tree
  Supply machine characteristics
  Analyze and auto-tune
    Flexible preservation, detection, and recovery
  Refine tradeoffs and repeat
  Execute and monitor
    CD management and coordination
    Distributed and hierarchical preservation
    Distributed and hierarchical recovery

## Slide 32
CD annotations express intent
  CD hierarchy for scoping and consistency
  Preservation directives and hints exploit locality
  Correctness abstractions
    Detectors and tolerances
  Recovery customization
  Debug/test interface
Work in progress: http://lph.ece.utexas.edu/users/CDAPI

## Slide 33
State preservation and restoration API
  curCD->Preserve(ptr,size,method_mask, byref_name, name, regenObj);
  Hierarchical
    Per CD (level)
    Match storage hierarchy
    Maximize locality and minimize overhead
  Proportional
    Preserve only when worth it (skip preserve calls)
    Exploit inherent redundancy
    Utilize regeneration
Notes: Different error mechanisms can be dealt with different storage.
Containment domains give you explicit control on this.
Distributed, hierarchical and partial state preservation saves bandwidth and power.
Partial preservation is very easy to express with containment domains.
Containment domains are analyzable and can be automatically tuned.
Explain preserve only when worth it
You don’t want to preserve everything for every error mechanism.
--------------------------------------------
Mainpoint: Distributed, hierarchical and partial state preservation saves bandwidth and power.
Mainpoint:
Mattan: partial preservation reduces overheads substantially and is very easy to express (preserve_via_parent and/or escalate). Also add that this can be analyzed and auto-tuned.
Mix with SPMV example.
Stress that this is the main advantage of CDs in terms of performance.
Give an example of SpMV (natural redundancy)
-----------------------------------
This preservation need not be complete

## Slide 34: Hierarchical local recovery and partial preservation
Disk
Inter-cabinet NVM
Inter-node NVM
DRAM
Partial preservation via sibling, parent, or regeneration where appropriate
Notes: But CDs are better match for codes like neutron transport where structure of the code looks like a tree of tasks. And there are fewer global synchronization points.
-----------------------------------------
Leaves don’t preserve these.
Naturally recover from above.
Again, it’s not that you can not do this today
Accessable and auto-tuned interface.
Machine specific can be tuned with CDs.
Mainpoint: Point is that these span a range of behavior. Not comprehensive, but still a range
After strengths slids, give example how the mini apps were analyzable. (pick one application)
A Monte Carlo approach to the simulation of neutron transport is desirable because the creation and simulation of every particle is independent, making the problem embarrassingly parallel.
HPCCG is a linear system solver that uses the
conjugate gradient method and can scale to a large number
of nodes
How we came up with the machines. (how we scaled)
Theoretical machines.
Mention containment domain we selected was based on auto tuning.
From these workloads we extracted containment domain structures and tuned it with our tools. (preservation intervals… and stuffs)
Synthetic application of
Each CDs annotated with
Mention it matches with SCR paper.
Mention everything is tuned with our tools (optimum interval)
Mantevo
NT is more like a tree of tasks
Leaves don’t preserve these.
Naturally recover from above.
Again, it’s not that you can not do this today
Accessable and auto-tuned interface.
Machine specific can be tuned with CDs.
Mainpoint: Point is that these span a range of behavior. Not comprehensive, but still a range
After strengths slids, give example how the mini apps were analyzable. (pick one application)
A Monte Carlo approach to the simulation of neutron transport is desirable because the creation and simulation of every particle is independent, making the problem embarrassingly parallel.
HPCCG is a linear system solver that uses the
conjugate gradient method and can scale to a large number
of nodes
How we came up with the machines. (how we scaled)
Theoretical machines.
Mention containment domain we selected was based on auto tuning.
From these workloads we extracted containment domain structures and tuned it with our tools. (preservation intervals… and stuffs)
Synthetic application of
Each CDs annotated with
Mention it matches with SCR paper.
Mention everything is tuned with our tools (optimum interval)
Mantevo

## Slide 35
Local copy or regen
Sibling
Parent (unchanged)

## Slide 36
Correctness abstractions
  Detectors
  Requirements
  Recovery

## Slide 37
What can go wrong?
  Application crash
  Process crash
  Process unresponsive
  Failed communication
  Hardware
    Cache error
    Memory error
    TLB error
    Node offline
    …

## Slide 38
What can go wrong?
  Lost resource
  Wrong value
    Specific address?
    Specific access?
    Specific computation?
  Degraded resource
Who detects?
How reported?

## Slide 39
Today: machine check architecture
  (Maskable) interrupts
  Complex encoding of errors / failures
    Spread across many processor-specific state registers
    Very difficult to parse and use
  Currently – level of containment reported
    Enables fine-grained software recovery
    Know before state is corrupted
    Know when only process state is corrupted
  Event counters and triggers for errors
    Root cause analysis

## Slide 40
Today: machine check architecture
  Not suitable for programmers
    Barely suitable for system implementers
    Doable, but tricky and requires a lot of reading
  Varies by vendor
  Continuously updated

## Slide 41
System-provided detectors
  curCD->Detect();
    Control response granularity
User-specified detectors
  curCD-> CDAssert(test, error_to_report);
Consistent and unified reporting & analysis

## Slide 42
Catch the error as soon as possible
  Less to recover
  Ideally smaller and faster preservation
  Micro-rollbacks
  Idempotent regions
  Hardware-level rollbacks

## Slide 43
Idempotent regions and hardware-rollback
  What if hardware can automatically rollback and rexecute?
    Fine-grained recovery will have little impact on performance
    Users may not need to do anything

## Slide 44
Instruction retry
  Out-of-order processors
  In-order and GPUs?

## Slide 45
Sophisticated out-of-order offer ample opportunity for hardware retry
  Speculative execution can be used to recovery from soft errors
  ROB and LSQ buffer temporary results
  Transactional memory does to

## Slide 46
Harder in a GPU
  Need to ensure effect-free rollback
    No hardware buffering
  Idempotent regions and CDs
  Tradeoffs with hardware buffering and detection latency

## Slide 47
Express correctness intent
  curCD-> RegisterDetection(errors_reported);
    Notifies auto-tuner of detection capability
    Enables error elision
  curCD->RequireErrorProbability( error_type, num_errors, probability,detect_or_fail_over);
    Auto- add redundancy to meet requested level of reliability
  curCD->GetErrorProbability( error_type, num_errors);
    Customize action

## Slide 48
Analogues to approximate computing research
  Compiler techniques for approximate computing
  Propagate loss of accuracy
  Propagate loss of reliability

## Slide 49
Debug, test, and tools
  Error and failure injection
  Planned integration with low-level injection
  CD profiler, viz, models, and initial tuner in place

## Slide 50
Quick(ish) way to search the error space
  Multi-mode simulation
  Skip over detectable errors
  Tool to be released
    Uses only public tools

## Slide 52: Machine and error models
Component | “Performance” | Error | Error Scaling
Core | 10GFLOP/core | Soft error | ∝ #cores
Memory | 1GB/core | ECC fail | ∝ #DRAM chips
Socket | 200GB/s /socket | Hard/OS crash | ∝ #sockets
System | Hierarchical network | Power module or network | ∝ #modules and #cabinets
Notes: We made this basic machine to different scales. We fixed performance and memory capacity per core. We varied the network bandwidth depending on the degrees of hierarchies we have in the machines.
Constant Fit rate for soft errors per core, memory errors per DRAM chip, system level failures per socket, and Power network failure per power distribution model.
-------------------------------------------------
Theoretical machines.
Mattan: Missing figure for system. That’s also the place to say weak scaling.
A Monte Carlo approach to the simulation of neutron transport is desirable because the creation and simulation of every particle is independent, making the problem embarrassingly parallel.
HPCCG is a linear system solver that uses the
conjugate gradient method and can scale to a large number
of nodes
How we came up with the machines. (how we scaled)
Theoretical machines.
Mention containment domain we selected was based on auto tuning.
From these workloads we extracted containment domain structures and tuned it with our tools. (preservation intervals… and stuffs)
-----------------------
Picture of the system.
Swimlanes. Big core style small core style.

## Slide 53
Input 1: machine configuration
  Physical and storage hierarchies (capacity and BW)
  Error/failure rates at each level of hierarchy
  Simple power model
Input 2: application description
  CD tree, including loops of CDs
  Preservation volumes and possible method
  Overlap of preservation and detection with parent
  Execution time estimate
Analytic model for CD behavior
  Overheads from preservation, detection, and recovery
Output efficiency
  Performance, energy, memory

## Slide 54: Error Failure Recovery

## Slide 55: Analytic Model
Leverage hierarchy and CD semantics
  Uncoordinated “local” actions
  Solve in  out
Application abstracted to CDs
  CD tree
  Volumes of preservation, computation, and communication
  Preservation and recovery options per CD
Machine model
  Storage hierarchy
  Communication hierarchy
  Bandwidths and capacities
  Error processes and rates
Execution time
Notes: Main Points: Abstraction made capturing existing resilience techniques and semantics of containment domain made analysis easy.
- Error rates would be sum of multiple error sources.
- Erroneous data never communicated -> we can evaluate one domain with children at a time. -> Go up to root -> you get the expected execution time.
Duration, error rate, hierarchy -> expected execution time.
One level at a time -> Recursively go to root.

## Slide 56: Power model
CDs that are not re-executing may remain idle
Actively executing a CD has a relative power of 1
A node that is idling consumes a relative power of
  In our experiments
Idle
Re-execution time
Parallel domains
Execution
Re-execution
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Idle
Notes: Added first order power model that takes into account nodes that are idle while waiting for other nodes to recover.
Power model can be improved with additional mapping information.

## Slide 57
SPMD-oriented analytical model and tuner
  Extrapolated profile
  Machine characteristics
  Tuning space and models

## Slide 58
Auto-tuned cross-layer resilience!
  Iterate with error injection
  Intelligent search exploration

## Slide 59
Execution model progress
  Building systems is hard and tricky
  Limited release of single-node runtime
  MPI runtime very close
    Lots of distributed programming issues
    Lots of current sad state of FT issues
  Open source soon on Bitbucket
    Initially only for soft errors

## Slide 60
Already useful and collaborations in progress
  Reaching down to hardware in FF2
  Global address space with DEGAS
  Task-based execution in Legion and SWARM
  DSL-facing in Stanford’s PSAAP II
  Algorithmic approach within TOORSES

## Slide 61
TOORSES fault-tolerant hierarchical solver
  Brian Austin, Eric Roman, and Xiaoye (Sherry) Li LBNL
  Hierarchical semi-separable representation

## Slide 62
Add CDs at different granularities
  Hierarchical and partial preservation
Add algorithmic and cheap detection
Compare to:
  Algorithmic recovery with redundant computation
Chart: Error injection rate (#/s)
| 1E-3 | 3.16E-3 | 0.01 | 3.1600000000000003E-2 | 0.1 | 0.316 | 1
Coarse | 0.99882 | 0.99738 | 0.9929 | 0.97894 | 0.93482 | 0.80892 | 0.51909
Medium | 0.9989 | 0.99797 | 0.99573 | 0.98792 | 0.96665 | 0.89821 | 0.71013
Fine | 0.99439 | 0.99432 | 0.99438 | 0.99413 | 0.99377 | 0.99268 | 0.98927
Encoded | 0.99679 | 0.9968 | 0.99656 | 0.99596 | 0.99477 | 0.99064 | 0.97818

## Slide 63: LULESH CD mapping example

## Slide 64: Autotuned CDs perform well
Peak System Performance
NT
SpMV
HPCCG
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.99175 | 0.98422 | 0.98302 | 0.97237 | 0.96043 | 0.94702 | 0.9429
h-CPR, 80% | 0.98845 | 0.98064 | 0.96938 | 0.94865 | 0.90855 | 0.85606 | 0.81179
g-CPR, 80% | 0.90834 | 0.80169 | 0.58706 | 0.17499 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.99042 | 0.98738 | 0.98262 | 0.97316 | 0.95456 | 0.93866 | 0.92273
h-CPR, 50% | 0.99086 | 0.98467 | 0.97572 | 0.9592 | 0.92711 | 0.88463 | 0.84863
g-CPR, 50% | 0.92719 | 0.84165 | 0.66711 | 0.32226 | 0 | 0 | 0
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 0.99996 | 0.99984 | 0.99971 | 0.99903 | 0.99638 | 0.99338 | 0.98936
h-CPR, 10% | 0.9959 | 0.99312 | 0.98908 | 0.98158 | 0.9669 | 0.94711 | 0.92649
g-CPR, 10% | 0.96711 | 0.92764 | 0.84441 | 0.67062 | 0.32739 | 0.075116 | 0
Notes: Mention initial results are very promising.
Why we chose 50% 80% and all that.
Show that there are three application
Mention clear bar. Mention what bars mean. Talk about legends (performance efficiency and energy overhead)
Add slides
Machine model
And error model.
--------------------------------
H-CPR is the name we used .. Like SCR
CDs can express h-cpr and we validated results with SCR paper.
Highlight 50% line.
Separate energy and performance
NT does very well because why it does well.
SpMV we only do partial preservation. That’s why it is doing well.
Question will be asked.
Why NT does well why Spmv does well. Explain it.

## Slide 65: CDs improve energy efficiency at scale
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.0063317 | 0.0087139 | 0.011899 | 0.01684 | 0.031066 | 0.034466 | 0.03948
h-CPR, 80% | 0.011686 | 0.019745 | 0.031588 | 0.054126 | 0.10065 | 0.16815 | 0.23184
gCPR, 80% | 0.10092 | 0.24736 | 0.70342 | 4.7145 | 0 | 0 | 0
Peak System Performance
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.009667 | 0.012778 | 0.017659 | 0.027499 | 0.047447 | 0.065194 | 0.083517
h-CPR, 50% | 0.0092258 | 0.015573 | 0.024881 | 0.042531 | 0.078624 | 0.13041 | 0.17836
g-CPR, 50% | 0.078529 | 0.18815 | 0.49901 | 2.1031 | 0 | 0 | 0
Chart: Energy Overhead
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 3.2383e-05 | 0.00011761 | 0.00012313 | 0.00031516 | 0.0010207 | 0.0029016 | 0.0063734
h-CPR, 10% | 0.0041141 | 0.0069317 | 0.011044 | 0.018769 | 0.034233 | 0.055844 | 0.079342
g-CPR, 10% | 0.034009 | 0.078008 | 0.18426 | 0.49115 | 2.0545 | 12.3128 | 0
NT
SpMV
HPCCG
Notes: What is the energy overhead?
Energy overhead is an overhead for preservation restoration and re-execution.

## Slide 66: 10X failure rate emphasizes CD benefits
Peak Performance
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, NT | 0.97429 | 0.95249 | 0.94834 | 0.91909 | 0.88349 | 0.84948 | 0.84043
h-CPR, 80% | 0.96389 | 0.93989 | 0.90594 | 0.84509 | 0.73378 | 0.59869 | 0.50114
CDs, NT | 0.020111 | 0.027491 | 0.037868 | 0.05341 | 0.09999 | 0.11288 | 0.12931
h-CPR, 80% | 0.037468 | 0.063959 | 0.10383 | 0.18331 | 0.36281 | 0.67032 | 0.99546
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, SpMV | 0.97682 | 0.96312 | 0.94625 | 0.91695 | 0.86188 | 0.81631 | 0.77161
h-CPR, 50% | 0.97135 | 0.95221 | 0.92492 | 0.87564 | 0.78093 | 0.66871 | 0.58205
CDs, SpMV | 0.023707 | 0.038222 | 0.056592 | 0.090147 | 0.15966 | 0.22445 | 0.29511
h-CPR, 50% | 0.029496 | 0.050187 | 0.081176 | 0.14202 | 0.28052 | 0.49541 | 0.71805
Chart: Performance Efficiency
| 2.5PF | 10PF | 40PF | 160PF | 640PF | 1.2EF | 2.5EF
CDs, HPCCG | 0.99981 | 0.99928 | 0.99767 | 0.99115 | 0.97793 | 0.97428 | 0.95844
h-CPR, 10% | 0.98709 | 0.97837 | 0.96563 | 0.94241 | 0.89351 | 0.83079 | 0.75137
CDs, HPCCG | 8.6689e-05 | 0.00031038 | 0.00069738 | 0.0024087 | 0.015272 | 0.018858 | 0.028328
h-CPR, 10% | 0.013076 | 0.022107 | 0.035589 | 0.061107 | 0.11918 | 0.20367 | 0.3309
Energy Overhead
Notes: If error rate is higher CDs become much more improtant.
Say
Paper includes other sensetivity
Mattan: Same as above about characteristics – reinforce your points.
Correct the legend
The reason why we experimented with higher rate. (scalability or? High altitude? )
Machine model.
Mention why we did 10x failure rate.

## Slide 67
What if my application has many barriers?
  Can’t really form a tree?

## Slide 68: SPMV: local recovery and partial preservation
Disk
Remote NVM
Local NVM
DRAM
Partial preservation via sibling or parent where appropriate
Notes: This one for the most part is similar to a scalable checkpoint restart we still have the advantage of some aspects of partial preservation because we can preserve some things with that are already preserved in the parent or with the natural redundancy.
Mainpoint: Point is that these span a range of behavior. Not comprehensive, but still a range
After strengths slids, give example how the mini apps were analyzable. (pick one application)
A Monte Carlo approach to the simulation of neutron transport is desirable because the creation and simulation of every particle is independent, making the problem embarrassingly parallel.
HPCCG is a linear system solver that uses the
conjugate gradient method and can scale to a large number
of nodes
How we came up with the machines. (how we scaled)
Theoretical machines.
Mention containment domain we selected was based on auto tuning.
From these workloads we extracted containment domain structures and tuned it with our tools. (preservation intervals… and stuffs)
Synthetic application of
Each CDs annotated with
Mention it matches with SCR paper.
Mention everything is tuned with our tools (optimum interval)
Mantevo

## Slide 69: Inter-CD communication?
Relaxed CDs enable inter-CD communication
  Maintain CD semantics w/ uncoordinated recovery
  Some data “preserved” via logging
  All communicated data still verified to be correct
Strict CDs do not communicate
  Only communicate when in same CD context
  Overheads for strict containment can be high
Outer CDs
Inner CDs
Sync+ comm

## Slide 70: SPMV: local recovery and partial preservation
Disk
Remote NVM
Local NVM
DRAM
Partial preservation via sibling or parent where appropriate
Relaxed CDs
Notes: This one for the most part is similar to a scalable checkpoint restart we still have the advantage of some aspects of partial preservation because we can preserve some things with that are already preserved in the parent or with the natural redundancy.
Mainpoint: Point is that these span a range of behavior. Not comprehensive, but still a range
After strengths slids, give example how the mini apps were analyzable. (pick one application)
A Monte Carlo approach to the simulation of neutron transport is desirable because the creation and simulation of every particle is independent, making the problem embarrassingly parallel.
HPCCG is a linear system solver that uses the
conjugate gradient method and can scale to a large number
of nodes
How we came up with the machines. (how we scaled)
Theoretical machines.
Mention containment domain we selected was based on auto tuning.
From these workloads we extracted containment domain structures and tuned it with our tools. (preservation intervals… and stuffs)
Synthetic application of
Each CDs annotated with
Mention it matches with SCR paper.
Mention everything is tuned with our tools (optimum interval)
Mantevo

## Slide 71: Fun with logging protocols

## Slide 72
What about tasks?
  CDs are great natural fit
    CDs + Legion
      Stanford project led by Alex Aiken
    CDs + Swarm
      Spinoff from UDel led by Guang Gao
    Perhaps also with *SS / Nachos
      Barcelona Supercomputing Centers

## Slide 73
Legion resilience
  Propagate failures up the dependence chain
  Utilize region copies to minimize reexecutions

## Slide 74
Legion + CDs resilience
  Model-guided management of copies
  Optimized reexecution propagation stop points
  Detection and specification semantics
  Integration with other resilience mechanisms

## Slide 75
Use Legion copies for CD preservation
Optimize for efficiency
  When to add copies
  Where to put copies to survive failures
  When to free copies
Account for different failure modes and rates

## Slide 77
Assumption/fear: reliability bounds performance
  Errors may corrupt results and failures kill applications
What is the error rate?
  Like today: keep ignoring the problem
  Much higher: need detection and recovery
  CDs abstract, scalable, and tunable
What is the failure rate?
  Like today: hierarchical checkpoint restart
  Higher: specialize preservation and recovery
  CDs are portable and tunable
Is it really a problem?
  CDs are general and analyzable
  CDs are composable?

## Slide 78: Conclusion
Containment domains
  Abstract constructs for resilience concerns & techniques
  Proportional and application/machine tuned resilience
  Hierarchical & distributed preservation, and recovery
  Analyzable and amendable to automatic optimization
  Scalable with high relative energy efficiency
  Heterogeneous to match emerging architecture
http://lph.ece.utexas.edu/public/CDs
Notes: Containment domains are abstract constructs for resilience concerns and techniques.
Containment domains are proportional and application and machine tuned resilience.
Containment domains provide hierarchical and distributed preservation, restoration and recovery.
Containment domains are analyzable and amendable to automatic optimization.
Containment domains are scalable to large system with high relative energy efficiency.
Containment domains match emerging heterogeneous architecture.

## Slide 79
Thank You!
  Please find the slides at https://lph.ece.utexas.edu/merez/MattanErez/ExacaleResilienceShort0715